## Slide 1: “Audio Compression “ Report
Made by : Ahmed Mahmoud Abdulfattah Ahmed
Bench No : 10
Section No : 1

## Slide 2: Why we need to develop audio compression techniques ?
The motivation for the development of many of these perceptual coders was their
potential application in broadcast multimedia. However, their major impact has been in the
distribution of audio over the Internet.
We live in an environment rich in auditory stimuli. Even an environment described as
quiet is filled with all kinds of natural and artificial sounds. The sounds are always present and come to us from all directions. Living in this stimulus-rich environment, it is essential that we have mechanisms for ignoring some of the stimuli and focusing on others.

## Slide 3
Over the course of our evolutionary history we have developed limitations on what we can hear. Some of these limitations are physiological ( depend on the physical form of us ), based on the machinery of hearing. Others are psychological ( depend on our not physical form , but “ hidden “ processes in us ) , based on how our brain processes auditory stimuli. The insight of researchers in audio coding has been the understanding that these limitations can be useful in selecting information that needs to be encoded and information that can be discarded. The limitations of human perception are incorporated into the compression process through the use of psychoacoustic models. We briefly describe the auditory model used by the most popular audio compression approaches.

## Slide 4: What is the main factor of our machinery of hearing mechanism ?
The machinery of hearing is frequency dependent. The variation of what is perceived as
equally loud at different frequencies was first measured by Fletcher and Munson at Bell Labs
in the mid-1930s . These measurements of perceptual equivalence were later refined by
Robinson and Dadson. Clearly, what two people think of as equally loud will be different. Therefore,
these curves are actually averages and serve as a guide to human auditory perception. The
particular curve that is of special interest to us is the threshold-of-hearing curve. This is the SPL
curve that delineates the boundary of audible and inaudible sounds at different frequencies.

## Slide 5: The main techniques for audio compression :
MPEG family techniques : known as Layer I, Layer II, and Layer III. The Layer III audio
compression algorithm is also referred to as mp3.
Layer 1 compression ratio : 4:1
Layer 2 compression ratio : 8:1 or 6:1
Layer 3 ( MP3) compression ratio : 10:1
The major difference between the Layer I and Layer II coding schemes is in the quantization
step. In the Layer I coding scheme the output of each subband is quantized using one of 14
possibilities; the same 14 possibilities are available for each of the subbands.

## Slide 6
In Layer II :
coding the quantizers used for each of the subbands can be selected from a different set of
quantizers depending on the sampling rate and the bit rates. For some sampling rate and bit
rate combinations, many of the higher subbands are assigned 0 bits. That is, the information
from those subbands is simply discarded. Where the quantizer selected has 3, 5, or 9 levels,
the Layer II coding scheme uses one more enhancement.
Layer III coding, which has become widely popular under the namemp3, is considerably more
complex than the Layer I and Layer II coding schemes. One of the problems with the Layer I
and II coding schemes was that with 32-band decomposition, the bandwidth of the subbands at
lower frequencies is significantly larger than the critical bands.

## Slide 7
If we get a high amplitude tone within a subband and if the subband is narrow enough, we can assume that it masked other tones in the band. However, if the bandwidth of the subband is significantly higher than the critical bandwidth at that frequency, it becomes more difficult to determine whether other tones in the subband will be masked.
A simple way to increase the spectral resolution would be to decompose the signal directly
into a higher number of bands. However, one of the requirements on the Layer III algorithm
is that it be backward compatible with Layer I and Layer II coders. To satisfy this backward
compatibility requirement, the spectral decomposition in the Layer III algorithm is performed
in two stages.

## Slide 8
First the 32-band subband decomposition used in Layer I and Layer II is
employed. The output of each subband is then transformed using a modified discrete cosine
transform (MDCT) with a 50% overlap. The Layer III algorithm specifies two sizes for the
MDCT, 6 or 18. This means that the output of each subband can be decomposed into 18
frequency coefficients or 6 frequency coefficients.
Because of this high level of compression of MP3 compression :
most people cannot tell the difference between the original and the compressed representation.
This development process has made MP3 the format of choice for compressed
music.

## Slide 9: Can we modify MP3 Mechanism ? How ??
The MPEG Layer III algorithm has been highly successful. However, it has some built-in
drawbacks because of the constraints under which it was designed. The principal constraint
was the requirement that it be backward compatible. This requirement for backward compatibility
forced the rather awkward decomposition structure involving a subband decomposition
followed by an MDCT decomposition. The period immediately following the release of the
MPEG specifications also saw major developments in hardware capability. The Advanced
Audio Coding (AAC) standard was approved as a higher quality multichannel alternative to
the backward compatible MPEG Layer III in 1997.

## Slide 10
The AAC standard takes a modular approach based on a set of self-contained tools or
modules. Some of these tools are taken from the earlier MPEG audio standard while others
are new. As with previous standards, the AAC standard actually specifies the decoder.
By using some or all of these tools(The decoder tools specified in the AAC standard ), the standard describes three profiles. These are the main profile, the low complexity profile, and the sampling-rate-scalable profile. The AAC approach used inMPEG-2was later enhanced and modified to provide an audio coding option in MPEG-4. In the following section we first describe the MPEG-2 AAC algorithm, followed by the MPEG-4 AAC algorithm.

## Slide 11: MPEG-2 AAC small overview :
Because the AAC algorithm is not backward compatible it does away with the requirement of
the 32-band filter bank. Instead, the frequency decomposition is accomplished by a modified
discrete cosine transform (MDCT). TheMDCTis described in Chapter 13. TheAACalgorithm
allows switching between a window length of 2048 samples and 256 samples. These window
lengths include a 50% overlap with neighboring blocks. So 2048 time samples are used to
generate 1024 spectral coefficients, and 256 time samples are used to generate 128 frequency
coefficients.
The quantization and coding strategy used in AAC is similar to what is used in MPEG Layer
III. Scalefactors are used to control the quantization noise as part of an outer distortion control
loop.

## Slide 12
The quantization step size is adjusted to accommodate a target bit rate in an inner rate
control loop. The quantized coefficients are grouped into sections. The section boundaries
have to coincide with scalefactor band boundaries. The quantized coefficients in each section
are coded using the same Huffman codebook. The partitioning of the coefficients into sections
is a dynamic process based on a greedy merge procedure. The procedure starts with the
maximum number of sections. Sections are merged if the overall bit rate can be reduced by
merging. Merging those sections will result in themaximum reduction in bit rate. This iterative
procedure is continued until there is no further reduction in the bit rate.

## Slide 13: MPEG-4 AAC small overview :
MPEG-4 AAC ( an update of MPEG-2 AAC ) adds a perceptual noise substitution (PNS) tool and substitutes a long term prediction (LTP) tool for the interband prediction tool in the spectral coding block. In the quantization and coding section MPEG-4 AAC adds the options of Transform-Domain Weighted Interleave Vector Quantization (TwinVQ) and Bit Sliced Arithmetic Coding (BSAC).

## Slide 14: Other techniques for audio compression:
We have described a number of audio compression approaches that make use of the limitations
of human audio perception. These are by no means the only ones. Competitors to DolbyDigital
include Digital Theater Systems (DTS) and Sony Dynamic Digital Sound (SDDS). Both of
these proprietary schemes use psychoacoustic modeling. The Adaptive TRansform Acoustic
Coding (ATRAC) algorithm was developed for the MiniDisc by Sony in the early 1990s,
followed by enhancements inATRAC3 andATRAC3plus. As with the other schemes described
in this report, the ATRAC approach uses MDCT for frequency decomposition, though the
audio signal is first decomposed into three bands using a two-stage decomposition.

## Slide 15
As in the case of the other schemes, the ATRAC algorithm recommends the use of the limitations of
human audio perception in order to discard information that is not perceptible.
Another algorithm that also uses MDCT and a psychoacoustic model is the open source
encoder Vorbis. The Vorbis algorithm also uses vector quantization and Huffman coding to
reduce the bit rate.

## Slide 16: References :
Khalid Sayood, “Introduction to Data Compression”, Fourth Edition, Elsevier 2012. [chapter 17]